MATLAB Programmer’s Guide for LCLS physicists

(Version 0.8)

9/22/08

0 REQUIREMENTS...............................................................................................................................4

1 BASICS .................................................................................................................................................5

1.1 SETTING UP THE ENVIRONMENT ....................................................................................................5

1.2 STARTING MATLAB ....................................................................................................................5

1.3 DIRECTORIES.................................................................................................................................5

1.4 CVS ..............................................................................................................................................5

1.4.1 Basic concept...........................................................................................................................5

1.4.2 CVS Commands .......................................................................................................................6

1.4.2.1 Checkout ...................................................................................................................................... 6

1.4.2.2 Commit ........................................................................................................................................ 6

1.4.2.3 Update.......................................................................................................................................... 6

1.4.2.4 Add .............................................................................................................................................. 6

1.4.2.5 Remove ........................................................................................................................................ 6

1.4.2.6 Diff............................................................................................................................................... 6

1.4.2.7 Other commands .......................................................................................................................... 7

1.4.3 CVSWEB..................................................................................................................................7

1.4.4 Guidelines................................................................................................................................7

2 LABCA .................................................................................................................................................8

2.1 GENERAL CONCEPTS .....................................................................................................................8

2.1.1 Parameters and return values..................................................................................................8

2.1.2 Type .........................................................................................................................................8

2.1.3 Timestamp format ....................................................................................................................8

2.1.4 Exceptions................................................................................................................................8

2.1.5 Timeouts ..................................................................................................................................9

2.2 BASIC COMMANDS ........................................................................................................................9

2.2.1 lcaGet ......................................................................................................................................9

2.2.2 lcaPut, lcaPutNoWait ............................................................................................................10

2.3 MONITORS...................................................................................................................................11

2.3.1 lcaSetMonitor ........................................................................................................................12

2.3.2 lcaNewMonitorValue.............................................................................................................12

2.3.3 lcaClear .................................................................................................................................13

2.4 NETWORK-RELATED SETTINGS....................................................................................................13

2.4.1 Timeout ..................................................................................................................................14

2.4.2 Retry count.............................................................................................................................14

2.4.3 Default configuration.............................................................................................................15

2.5 OTHER.........................................................................................................................................15

3 AIDA ...................................................................................................................................................16

3.1 JAVA SETUP .................................................................................................................................16

3.2 BROWSING NAMES ......................................................................................................................16

3.3 RETRIEVING DATA.......................................................................................................................16

3.4 MISCELLANEOUS.........................................................................................................................18

4 BEAM SYNCHRONOUS ACQUISITION .....................................................................................19

4.1 RESERVING AN EVENT DEFINITION ..............................................................................................19

4.2 CHANGING DEFAULT PARAMETERS .............................................................................................20

4.3 STARTING DATA ACQUISITION.....................................................................................................20

4.4 RELEASING AN EVENT DEFINITION ..............................................................................................21

4.5 AN EXAMPLE SCRIPT ...................................................................................................................21

6 IMAGE MANAGEMENT ................................................................................................................23

6.1 OVERVIEW ..................................................................................................................................23

6.2 GLOBAL DATA.............................................................................................................................23

6.3 GUI APPLICATIONS .....................................................................................................................23

6.3.1 Image acquisition...................................................................................................................23

6.3.2 Image analysis .......................................................................................................................24

6.3.3 Image browser .......................................................................................................................24

6.4 CAMERA INITIALIZATION ............................................................................................................25

6.5 BUFFERED IMAGE ACQUISITION...................................................................................................25

6.6 RAW IMAGE PROCESSING ............................................................................................................26

6.7 OTHER FUNCTIONS ......................................................................................................................26

6.8 DATA STRUCTURES ......................................................................................................................27

6.8.1 Camera ..................................................................................................................................27

6.8.2 Dataset...................................................................................................................................27

6.8.3 ImgAnalysisData ...................................................................................................................28

6.8.4 ImgBrowserData ...................................................................................................................29

6.8.5 ImgManData..........................................................................................................................29

6.8.6 IpOutput.................................................................................................................................30

6.8.7 IpParam.................................................................................................................................30

6.8.8 RawImg..................................................................................................................................32

7 CMLOG..............................................................................................................................................34

7.1 STARTING CMLOG BROWSER .......................................................................................................34

7.2 LOGGING MESSAGES ...................................................................................................................34

8 MISCELLANEOUS FUNCTIONS ..................................................................................................35

8.1 LCA2MATLABTIME......................................................................................................................35

8.2 LCATS2PULSEID..........................................................................................................................35

9 AN EXAMPLE SESSION .................................................................................................................36

APPENDIX A MAD/EPICS/SLC NAMES .......................................................................................38

APPENDIX B EPICS/SLC ATTRIBUTES ......................................................................................43

9.1 MAGNET ATTRIBUTES .................................................................................................................43

APPENDIX C AIDA TYPES..............................................................................................................44

APPENDIX D TEST PVS...................................................................................................................45

0 Requirements

* A UNIX/AFS account

http://www2.slac.stanford.edu/comp/slacwide/account/account.html

* A Red Hat 4 (or compatible linux) machine to log onto, e.g.

lcls-dev2.slac.stanford.edu

1 Basics

1.1 Setting up the environment

After you log onto a Linux machine using your AFS account for the first time, you have to add the following line to the file .cshrc in your home directory: source /afs/slac/g/lcls/tools/script/ENVS.csh

If you need access to OTR images or similar data, also append this line

setenv EPICS_CA_MAX_ARRAY_BYTES 40000000

If you log from Windows PC, you should also add the line:

setenv DISPLAY = your_IP_address:0

where your_IP_address can be found after e.g. running ipconfig on Windows. Note: All strings are case-sensitive.

1.2 Starting MATLAB

If you want the full development environment, type

matlab

to start the full GUI version If you want to run applications only and/or do some basic scripting (recommended), type

matlab -nodesktop -nosplash

to start the fully working command-line version that requires much less resources.

1.3 Directories

If you want to share your tested scripts, copy them to

/afs/slac/g/lcls/matlab/toolbox

MATLAB scripts from LCLS software engineering team are in

/afs/slac/g/lcls/matlab/script

1.4 CVS

You can use CVS to keep track of changes to your scripts, enable collaborative editing, compare to previous versions, etc.

1.4.1 Basic concept

CVS keeps up-to-date copies of your files in a single repository, and you along with other people work with copies of these files in a local directory. Think of CVS as a hypermodern library where you can edit books.

1.4.2 CVS Commands

All CVS commands follow the keyword cvs.

1.4.2.1 Checkout

To start working with CVS, you must check out a module (directory).

>> cvs checkout matlab/toolbox

1.4.2.2 Commit

After you made changes to a local file (and tested it), you can commit it back to the repository.

>> cvs commit matlab/toolbox/moments.m

Don’t forget to enter a short, but comprehensive comment!

1.4.2.3 Update

You can update your local directory with files from the repository, if you didn’t change their content yet.

>> cvs update cvs update: Updating matlab

1.4.2.4 Add

If you created a new local file, you can put it into the CVS repository.

>> cvs add matlab/toolbox/hist2.m

1.4.2.5 Remove

If you removed a local file, you can remove it from the CVS repository.

>> cvs remove matlab/toolbox/hist2.m

1.4.2.6 Diff

Sometimes you want to know how your local files differ from the ones in the repository.

>> cvs diff matlab/toolbox/hist2.m

1.4.2.7 Other commands

See for a comprehensive list of other CVS commands here

http://www.cvsnt.org/wiki/CvsCommand

1.4.3 CVSWEB

There is a website that gives you graphical access to the CVS repository

www.slac.stanford.edu/cgi-wrap/cvsweb/matlab/toolbox/?cvsroot=LCLS

1.4.4 Guidelines

Some good guidelines for using CVS can be found here

http://dotat.at/writing/cvs-guidelines.html

2 LabCA

Interface to EPICS, the LCLS control system

The labCA toolbox wraps the essential ChannelAccess routines and makes them accessible from the MATLAB programs.

2.1 General concepts

2.1.1 Parameters and return values

All labCA calls take a PV argument identifying the EPICS process variable the user wants to access. EPICS PVs are plain ASCII strings that follow the pattern

<device>:<attribute>

LabCA is capable of handling multiple PVs in a single call; they are simply passed as a cell-array of strings, e.g.:

pvs = { 'device:xyz'; 'PVa'; 'anotherone' }

2.1.2 Type

Unless all PVs are of native ‘string’ type or conversion to ‘string’ is enforced explicitly (type char), labCA always converts data to double. Legal values for type are byte, short, long, float, double, native, or char (for strings).

2.1.3 Timestamp format

ChannelAccess timestamps provide the number of nanoseconds since 00:00:00 UTC, January 1, 1970. LabCA translates the timestamp into a complex number with the seconds in the real and nanoseconds in the imaginary parts. To convert timestamps into MATLAB format use epics2matlabTime (see 8.1).

2.1.4 Exceptions

If a labCA command cannot execute correctly, it prints an error message and throws an exception. If the exception is not caught, the execution is aborted (look for details in the MATLAB manual).

>> try lcaGet('gibberish') catch 'Reading from PV ''gibberish'' produced this error' end multi_ezca_get_nelem -ezcaGetNelem(): could not find process variable

: gibberishError: Errors encountered...

ans =

Reading from PV 'gibberish' produced this error

2.1.5 Timeouts

Since labCA is used for accessing data via network, your function calls can timeout (see 2.4).

2.2 Basic commands

2.2.1 lcaGet

[value, timestamp] = lcaGet(pvs, nmax, type)

Description

Read a number of PVs.

Parameters

pvs

m x 1 cell-matrix of m strings.

nmax (optional) Maximum number of elements (per PV) to retrieve (i.e. limit the number of columns of value to nmax). If set to 0 (default), all elements are fetched and the number of columns in the result matrix is set to the maximum number of elements among the PVs. This parameter is useful to limit the transfer time of large waveforms.

type (optional) A string specifying the data type to be used for the channel access data transfer.

Returns

value

The m x n result matrix. n is automatically assigned to accommodate the PV with the most elements. Excess elements of PVs with less than n elements are filled with NaN values. LabCA fills the rows corresponding to INVALID PVs with NaNs. In addition, warning messages are printed to the console if a PV's alarm status exceeds a configurable threshold.

timestamp

m x 1 column vector of complex numbers holding the CA timestamps of the requested PVs. The timestamps count the number of seconds (real part) and fractional nanoseconds (imaginary part) elapsed since 00:00:00 UTC, Jan. 1, 1970.

Example

>> [values, timestamps] = lcaGet({'MIKE:BEAM'; 'MIKE:BEAM:RATE'}, 0, 'char')

values =

'ON' '1'

timestamps = 1.0e+09 * 1.1546 + 0.8052i

1.1546 + 0.5014i

>> timestamps(1), timestamps(2) ans = 1.1546e+09 + 8.0522e+08i

ans = 1.1546e+09 + 5.0136e+08i

2.2.2 lcaPut, lcaPutNoWait

lcaPut(pvs, value, type) lcaPutNoWait(pvs, value, type)

Description

Write values to a number of PVs, which may be scalars or arrays of different dimensions. It is possible to write the same value to a collection of PVs.

lcaPut will wait until the request is processed on the server, lcaPutNoWait returns immediately.

Parameters

pvs

m x 1 cell-matrix of m strings.

value

A matrix or a row array of values to be written to PVs. In latter case, the same value is written to all m PVs.

type (optional) A string specifying the data type to be used for the channel access data transfer (see 2.1.2)

Example

>> lcaPut('MIKE:BEAM:RATE', 5)

>> lcaGet('MIKE:BEAM:RATE')

ans =

5

2.3 Monitors

Background

There is often a case where you need to wait until a PV value changes. While the code below works

initialValue = lcaGet(‘waveformPV’);

while(1)

currentValue = lcaGet(‘waveformPV’);

if ~isequal(currentValue, initialValue)

%do somet

break;

end

end

unnecessary network traffic can be the result if waveformPV stores big amount of data. To counter, labCA allows you to ask whether a PV value has changed. Then, you get the new value using lcaGet.

2.3.1 lcaSetMonitor

lcaSetMonitor(pvs, nmax, type)

Description

Set a ”monitor” on a set of PVs. Use the lcaNewMonitorValue to check monitor status (local flag). If new data is available, it is retrieved using the lcaGet call. Use the lcaClear call to remove monitors on a channel.

Parameters

pvs

m x 1 cell-matrix of m strings.

nmax (optional) Maximum number of elements (per PV) to monitor. If set to 0, all elements are fetched.

type (optional) A string specifying the data type to be used for the channel access data transfer. The native type is used by default. The type specified for the subsequent lcaGet call should match the monitor's data type.

Example

>> lcaSetMonitor(‘MIKE:BEAM’)

2.3.2 lcaNewMonitorValue

[flags] = lcaNewMonitorValue(pvs, type)

Description

Check if monitored PVs need to be read, i.e. if fresh data is available (due to initial connection or changes in value and/or severity status). Reading the actual data must be done using lcaGet.

Parameters

pvs

m x 1 cell-matrix of m strings.

type (optional) A string specifying the data type to be used for the channel access data transfer. The native type is used by default. Note that monitors are specific to a particular data type and therefore lcaNewMonitorValue will only report the status for a monitor that had been established by lcaSetMonitor with a matching type.

Returns

flags

A cell-array of flag values. A value of 0 indicates that no new data is available the monitored PV has not changed since it was last read. A value of 1 indicates that new data is available for reading (with lcaGet). A negative flag value indicates a problem:

-1: no monitor established (lcaSetMonitor never called for this PV/data type) -2: non-existing PV (no successful CA search so far), -3: invalid type argument, -4: invalid PV argument, -10: currently no connection.

Example

>> lcaNewMonitorValue({'a';'b'})

ans =

-2

-2

2.3.3 lcaClear

lcaClear(pvs)

Description

Disconnect PVs. All monitors on the target channel(s) are cancelled/released as a consequence of this call.

Parameters

pvs (optional) m x 1 cell-matrix of m strings. If omitted, disconnects all PVs.

Example

>> lcaClear

2.4 Network-related settings

The default labCA timeout for ChannelAccess calls is 0.1s and the default number of retries is 299. This means that if something does not work on the server, the labCA commands will wait for up to 29.9s before they return. We recommend changing these values.

2.4.1 Timeout

currentTimeout = lcaGetTimeout()

Description

Retrieve current timeout (in seconds).

Returns

currentTimeout

Current timeout in seconds

lcaSetTimeout(newTimeout)

Description

Set the new timeout.

Parameters

newTimeout

New timeout in seconds.

Example

>> lcaSetTimeout(0.1)

>> lcaGetTimeout

ans =

0.1000

2.4.2 Retry count

currentRetryCount = lcaGetRetryCount()

Description

Retrieve the number of retries.

Returns

currentRetryCount

lcaSetRetryCount(newRetryCount)

Description

Set the number of retries.

Parameters

newRetryCount

Example

>> lcaSetRetryCount(10) >> lcaGetRetryCount

ans =

10

2.4.3 Default configuration

You may want to choose to include the default LCLS labCA configuration script lcaInit in your startup.m file. See MATLAB documentation for details.

2.5 Other

For all supported labCA commands see

http://www.slac.stanford.edu/~strauman/labca/manual/node2.html

3 AIDA

Interface to SLC model data

SLC model data (e.g. TWISS parameters) is not accessible via ChannelAccess. Instead, you must use the Java-based library called AIDA (Accelerator Integrated Data Access).

3.1 Java setup

Make sure you have a java.opts file in the directory from which you start MATLAB.

3.2 Browsing names

You can browse AIDA names by typing

aidalist(device, attribute)

As a temporary solution, this function will prompt for your password.

Parameters

device

AIDA device name attribute (optional)

AIDA attribute name

Note: As a wild character, you can use the % character (but NOT *). However, in the device parameter you must at least include one other character (also, be mindful of the output).

Returns

The output is a list of names known to AIDA.

Example

>> aidalist(‘QUAD:IM20:221’, ‘Z%’) chevtsov@flora’s password:

QUAD:IM20:221 Z QUAD:IM20:221 ZTIM

ans = 0

3.3 Retrieving data

To get data, use the function

aidaget(aida_name, type, params)

Parameters

aida_name

AIDA name following the pattern

<device>//<attribute>

Note: Device/attribute names used by AIDA differ from the ones used by EPICS, see Appendix A.

type

(optional) case-insensitive string. Choose type from the table in Appendix C.

params

(optional) a cell array of AIDA parameters. Use the “=” notation for each parameter and value.

Returns

SLC value(s) of the specified type

Example 1

>> aidaget('YCOR:PR12:1052//BACT', ‘double’)

Fri Sep 15 11:58:48 PDT 2006: Making connection to Name Service Fri Sep 15 11:58:48 PDT 2006: Making connection to daServer

ans =

0

Example 2

>> r = aidaget('BPMS:IA20:221//R', 'doublea', {'B=BPMS:IA20:511'}); Fri Sep 15 12:00:06 PDT 2006: Making connection to Name Service Fri Sep 15 12:00:06 PDT 2006: Making connection to daServer >> rMatrix = reshape(r, 6, 6)'

rMatrix =

Columns 1 through 3

| [ | -0.7087] | [ | 0.1886] | [-7.0392e-19] |
| --- | --- | --- | --- | --- |
| [ | 0.1703] | [ | -0.1078] | [ 1.6913e-19] |
| [ 4.6419e-19] | [-9.7456e-20] | [ | -0.4677] |
| [ 1.5362e-19] | [ 6.2426e-20] | [ | -0.1548] |
| [-2.5244e-29] | [-3.9345e-30] | [ | 0] |

[ 0] [ 0] [ 0]

Columns 4 through 6

| [ 1.8859e-19] | [0] | [-2.4379e-32] |
| --- | --- | --- |
| [-1.0779e-19] | [0] | [ 1.0095e-32] |
| [ | 0.0975] | [0] | [ | 0] |
| [ | -0.0624] | [0] | [ | 0] |
| [ | 0] | [1] | [-3.2001e-28] |
| [ | 0] | [0] | [ | 0.0443] |

3.4 Miscellaneous

For more information like possible parameters, please see

http://www.slac.stanford.edu/grp/cd/soft/aida

4 Beam synchronous acquisition

An LCLS event system has been setup to read devices synchronous with beam crossing, such as BPMS and toroids. This system can be used from within Matlab with a few simple calls. Note that this is not implemented for image data collection. See separate section on collecting image data and collecting image data along with other beam synchronous devices. Figure 4.1 shows how the IOC looks at the EVR signal and BPM data to fill its BSA buffers.

Figure 1: Conceptual data flow for Beam Synchronous Acquisition

4.1 Reserving an event definition

eDefNumber = eDefReserve(myName)

Description

Reserves an event definition for your use.

Parameters

myName

a unique name for your application

Returns

ID of an event definition

4.2 Changing default parameters

eDefParams (eDefNumber, navg, nrpos, incmSet, incmReset, excmSet, excmReset )

Description

Changes defaults of the supplied arguments

Parameters

eDefNumber

ID of an event definition

navg

Number of pulses to average per reading To reduce the amount of jitter, you may choose to average several pulses together to get an averaged value. Default is no averaging; maximum is currently 10.

nrpos

Number of readings to take, which is the buffer size you wish to acquire. Default is one reading; maximum is currently 2800.

incmSet, incmReset, excmSet, excmReset

Optional Inclusion and Exclusion Timing Modifiers. Specific PNET bits you wish to be present or absent during your acquisition, such as ONE_HERTZ. See the PNBN database for a list of available PNET bits by viewing the PVs MP00:PNBN:[1..150]:NAME. Defaults to the values in VX00:DGRP:1150:INCM and VX00:DGRP:1150:EXCM.

4.3 Starting data acquisition

elapsedTime = eDefAcq (eDefNumber, timeout)

Description

Starts the data acquisition cycle. If the elapsed time is less than the timeout specified then your buffers are completely populated with the number of readings you specified, otherwise your buffers are populated with the number of readings the system was able to collect in the time allotted for data acquisition. This function blocks Matlab execution. Please see the script for a non-blocking example.

You collect your data from PVs with lcaGet. If, for example, you're interested in the device BPMS:IN20:221, your data can be found in the following PVs:

BPMS:IN20:221:XHST[eDefNumber]

Waveform containing all BPMS X values collected

BPMS:IN20:22:1:X[eDefNumber]

The last BPMS X value collected, handy when you only requested one reading

BPMS:IN20:221:X[eDefNumber].H

Rms of the last BPMS X value collected

BPMS:IN20:221:MEASCNT[eDefNumber]

Number of beam pulses used in your acquisition

Data for all devices known to the event definition system is available. There is no need to specify a device list for data acquisition. For en explanation of all available devices, please see the documentation on event definitions. For a complete list of BSA pvs, please try the Aida query LCLS//* at https://seal.slac.stanford.edu/aidaweb

4.4 Releasing an event definition

eDefRelease (eDefNumber)

Description

Releases your event definition for use by another control system application. Note that you can perform many data acquisition and collection cycles before releasing your event definition reservation.

Parameters

eDefNumber

ID of an event definition

4.5 An example script

The example can be found in eDefExample.m

% Choose unique name

myName = 'Matlab eDef';

myNAVG = 1;

myNRPOS = 20;

timeout = 3.0; % seconds

% Reserve an eDef number