To:	Luchini, Kristi; Akre, Ronald A.; Williams Jr., Ernest L.; Shoaee, Hamid; Lahey, Terri E.; Spencer, Nancy; Paz, Joan A.; Underwood, Kenneth K.; Zelazny, Michael S.; Szalata, Zenon M.

Cc:	Peng, Sheng; Allison, Stephanie; White, Greg; Fairley, Diane; Rogind, Debbie; Krauter, Karey E.; MacKenzie, Ronald R.; Cecere, Michael A; Dusatko, John E.; Kotturi, Karen 'Dayle'; Alarcon, Arturo; Schuh, Stephen; Norum, Stephen; Browne, Mike J.

Subject:	RE: MCC Operations Status Report - Friday  Jan 18th 8am

MCC Operations Status Report

Friday January 18, 2008

Laser: Sheng and Zen

1. X-Corr shutter doesn't respond to controls.

2. All Laser Camera's have swapped lines ( line 1 with 2 and line 3 with 4, etc…)

3. Artemis #82439. OTR21 is not synced with beam at 1Hz when another profile monitor is in

4. Didn't have the status of the laser pps on the laser displays. There was a problem with a burn thru Monitor in the bsy and the machine was turned off but the laser people didn't know because there was no status on the displays.

_____________________________________________

From: 	Luchini, Kristi

Sent:	Friday, January 18, 2008 10:03 AM

To:	Luchini, Kristi; Akre, Ronald A.; Williams Jr., Ernest L.; Shoaee, Hamid; Lahey, Terri E.; Spencer, Nancy; Paz, Joan A.; Underwood, Kenneth K.; Zelazny, Michael S.; Szalata, Zenon M.

Cc:	Peng, Sheng; Allison, Stephanie; White, Greg; Fairley, Diane; Rogind, Debbie; Krauter, Karey E.; MacKenzie, Ronald R.; Cecere, Michael A; Dusatko, John E.; Kotturi, Karen 'Dayle'; Alarcon, Arturo; Schuh, Stephen; Norum, Stephen; Browne, Mike J.

Subject:	RE: MCC Operations Status Report - Friday  Jan 18th 8am

MCC Operations Status Report

Friday January 18, 2008

STATUS OF RF TIMING SHIFT: Seamless!!!!

Here's the message Jim Welsh put into the physics elog at 9:06am

Just before 9:00 Stefanie made a 117.6 ns timing change.

No laser  problems were observed. Beam came back with more energy and three klystrons were taken

offline to accommodate. Linac bpm timing checks show approximately the correct timing.

IMPORTANT MORNING NOTICE:  9am

RF Timing Shift Details:  from Ron Akre.

Stephanie Allison will make changes to the EVG database (I could be wrong here, but Steph will do something) which will cause the LCLS timing system to shift by 14 cycles of 119MHz later with respect to the linac timing system.  LCLS triggers will remain the same with respect to the LCLS injector and L1 beam.

This will be done to align the LCLS off axis injector and L1 beam to the location of where the beam should be in the main linac, LCLS L2 and L3.  The reason we are aligning the LCLS injector to the last 10 sectors of the linac (rather that the other way around) is so that we can retain the ability of accelerating beam through the full 30 sectors of the linac without retiming the last 10 sectors.

This mornings 8am meeting:

.

BPMS:  Nancy and Greg

Artimis  #82449, #82450, #82451

1. The Artimis BPM related problems are listed as CTRL but SWE is suspected, in particular SLCCAS and possibly BPM Sampler on VMS. Joan is extracting the SLCCAS image Aug 14, 2007 version from tape and Nancy plans will  restart the old version this morning.

2. Trouble access model data from bpm's from Aida. Greg looking into this last night and is in communication with Henrick

Aida process started up automatically on VMS after MCC was rebooted yesterday however, there were some problems with a couple of processes not working properly. Greg ran test program on the processes which check to see if each process is doing is job and he determined that a couple were not working.

Event: Stephanie - DONE

The EVG software released this before 8am this morning and the EVG IOC rebooted in order to move all delays for all triggers (all event codes) ahead by 14 ticks = 117.6 nsec. See MCC elog entry from Stephanie last night 17-Jan-2008 17:14 for more details

Laser: Sheng and Zen

X-Corr shutter doesn't respond to controls.

LLRF: Dayle and Ron Akre

1. RF timing shift this morning by 116 ns with respect to the LCLS injector.

This changes the arrival time of electrons in the Linac and will allow the machine to get more energy out.

2.Feedback changes this morning for 21-3. They will need some timing help.

Matlab: Henrick

Phase scan GUI doesn't bias L1X actual phase, so funny plot when PDES=-190 and PACT=170

Wire Scanners: Arturo  and Doug McCormick - in progress

1. WIRE:LI28:444 has wrong calibration for POSN field. Temporary fix in matlab program

2. PMT:LI28:744 doesn't see any signal from WIRE:LI28:744 and very low signal from upstream wires

3. PMTs triggered from Linac timing system, therefore no control on ADC delay and gate width

4. Wire scanners WIRE:LI27:644 and WIRE:LI28:744 are not accessible through AIDA for model data

SAFETY:

1. If anyone has had trouble going up/down the staircase in the linac sector 24 please contact Paul Miller x2939.

2. An lcls worker was injured last night and was taken to the hospital. Ops wats to send a reminder everyone to  please be careful.

- Kristi